## Slide 1: Climate Emulator
Data Selection Process
Goal: Explore change in local temperature extremes as a function of en-roads climate policy choices.

## Slide 2: Summary
Choose only one model to maintain interpretability of uncertainty
Scenario&variable selection needs to sufficiently cover function space of in-/output relation
Scenarios:
  Have at least 1pctCO2, 1pctCO2-dcr to study impulse response
  Have at least *-aer experiments to study aerosol response
In- and Output variables:
  Choose GHG inputs that interface with en-roads: constrained to global averages.
  Have at least surface air temperature (tas) output
  Have at least tasmin, tasmax as output variable if temporal resolution ≥ day
  Spatial resolution ≤ 1°
Wehner et al., Weather and Climate Extremes, 2020

## Slide 3: Summary outstanding questions
Which exact input variable(s) do we want?
  Emissions vs. concentrations
    Choose CO2 and CH4 emissions, because it‘ll make it easier to expand to aerosol emissions
  Local vs. global
    En-roads only has global resolution
    Choosing aerosol emissions only mostly matters with local resolution; but global aerosols also matter for unmasking. Local aerosols have impact on high-pollution countries such as China.
  Global temp vs. GHG emissions as input
    We can‘t trust en-roads globel temp. output
    Use GHG emissions, because there‘s other temporal factors that influence global mean, such as, ENSO
  Anthropogenic vs. non-anthropogenic
  co2, ch4, aerosols, co2e, vs. radiative forcing
  Q: Should we emulate local aerosols OR interface with en-roads?
  Aerosols:
    PDRMIP or CDRMIP has impulse responses per aerosol.
Which temporal resolution of in-/ and output is needed?

## Slide 4: Model selection
Choose only one model to maintain interpretability of uncertainty
Avoid „hot“ model, i.e., a model with over average climate sensitivity
Questions:
  Q: Should model have high precipitation skill according to [Wehner et al., 2020]?
    CNRM (-CM6-1-HR, -CM6-1, -ESM2-1), CESM2 (-WACCM), or NorESM2-MM have high skill.
  Q: Should model have high temperature skill according to [Wehner t al., 2020]?
    CESM2-WACCM has low skill.

## Slide 5: Scenario selection
List of Tier1 scenarios
Choose 1pctCO2, 1pctCO2-dcr to study impulse response
Choose *-aer experiments to study aerosol response
Choose as many as possible to increase data diversity
Only choose scenarios that keep non-input parameters and model fixed

## Slide 6: Input variable selection List of all variables
Choose only CO2
  Aerosols matter most on local scales
  CH4 matters on global scale, but will complicate mapping
  CO2e or radiative forcings are hard to calculate
We choose emissions, not concentrations
  En-roads outputs both
  If we choose concentrations, we‘ll rely on the en-roads integrated assesment model
  Choosing emissions, means we‘ll either need memory in the model or compute concentrations from emissions
  Choosing emissions will make adaptation to aerosols easier
Q: Which CO2 do we want?
  Q: Choose all co2 sources or only anthropogenic sources (which are varied by en-roads)
  Possible selection:
    co2mass: Total Atmospheric Mass of CO2 [kg]
    co2: Mole Fraction of CO2 [mol mol-1]
    co2s: Atmosphere CO2 [1e-06]
    emiXXX: Total Emission Rate of XXX
    fco2antt: Carbon Mass Flux into Atmosphere Due to All Anthropogenic Emissions of CO2 [kg m-2 s-1]
    fco2fos: Carbon Mass Flux into Atmosphere Due to Fossil Fuel Emissions of CO2 [kg m-2 s-1]
    fgco2: Surface Downward Flux of Total CO2 [kg m-2 s-1]
We choose global spatial resolution:
  Global is sufficient for CO2 and CH4, because they are well mixed
  Local resolution <= continent-scale needed for aerosols, but en-roads only has global
Temporal resolution (see output variable selection)

## Slide 7: Output variable selection List of all variables
Choose to start with surface temperatures:
  Q: which temperatures do we want?
    Start with
      tas: Near-Surface Air Temperature [K]
      tasmin&tasmax: Daily Min-& Maximum Near-Surface Air Temperature [K]
        Add if temporal resolution ≥ day
    Possible other selection from all variables:
      tdps: 2m Dewpoint Temperature [K] ?
      tnXX: Tendency of Air Temperature due to XXX?
      tos: Sea Surface Temperature [degC] ?
      wbptemp: Wet Bulb Potential Temperature [K] ?
Temporal resolution
  Q: choose 1-hourly, 3-hourly, daily, monthly or yearly resolution?
    Is yearly still relevant for stakeholders?
    Start with monthly?
    1- and 3-hr needed for autoregressive model, but difficult due to data availability and storage
  Q: or only predict snapshot at 2030, 2050, and 2100?
    Stakeholders might only care about a specific year.